# WPD SW ENGINEERING

Intel Corporation, 2800 Center Dr.
DuPont, WA 98327-5050

DATE:	Oct. 30, 1998

TO:	WPD Business Unit

CC:	

FROM:	WPD SWE Engineering

SUBJECT:	4M4SG0X0.86E Standard BIOS

# About This Release

- 4M4SG0X0.86E.0026.B.9810301106

# Features/Errata Fixed In This Release

# B-0026 (Tanner 500mhz support BIOS)

# Forced C6C/CK1 cacheable address range to 64GB always (was 512mb).

# Improved L2 knobs for Katmai/C6C (Tanner) 450 and 500MHz.

# Improved L2 knobs for Deschutes/C6C (P2XP) 400 and 450MHz.

# Added D46 errata workaround for Pentium II Xeon processor.

# P07-0025

# Changed 400MHz and 450MHz L2 latency to 10,1,1,1

# Fixed DRAM throttling control registers

# Fixed El Torito formatted CD-rom boot

# Fixed Recovery Mode when On PME set to Power On

# Fixed NMI enable

# Fix for WHQL PNP BIOS test failure

# Fixed APM standby problem in Win95

# Updated processor microcode for Intel Pentium ® Xeon ™ processors.

# Fixed intermittent wake On PME

# Fix for WHQL unreported memory failure under ACPI

# Added quiet boot support (small user logo support).

# Added SMBIOS 2.2 compliance.

# P06-0023

# Fix for WHQL APM 1.2 test failure (Suspend Resume Timer via RTC Alarm)

# Fix for WHQL APM 1.2 test failure for Suspend using IBM 10G IDE Drive

# Fix for WHQL ACPI test failure (Unreported memory 0FEC0 APIC)

# P05-0020

# Fixed ACPI wake on KBD

# Fixed wake on Ring

# Fixed STBL manufacturing test

# Fixed SMBIOS type 17 structures

# P04-0019

# Changed Manufacturing Default for the AC Power Loss CMOS bit to “Always On”.

# P03-0018

# Fixed problem that would cause PCI configuration space corruption resulting in system hangs.

# Fixed ACPI IRQ routing for USB device.

# Fixed ACPI/RTC compliance issue.

# Fixed issue related to IRQ 12 availability with disabled PS/2 mouse.

# Fixed SETUP access security inconsistencies for unattended start, clear user password and user setup access.

# Clarified boot order message in SETUP help text.

# Added Memory Decreased error logging and functionality.

# Removed ECC memory SETUP option.  The system now requires ECC memory.

# Fixed SETUP hard drive menu corruption.

# Fixed shutdown hang with some non-compliant ATAPI devices.

# Fixed SETUP display for HDD > 8.4 G.

# Fixed DMI memory structures.

# P02-0017

# Boot time for certain ATAPI devices reduced.

# Locked cmos.

# Hang when Win98 or Win95 shutdown fixed, related to ATAPI/IDE devices.

# ACPI ring indicator functional.

# Hard Disk Drive menu corruption fixed.

# ECC/Non-ECC removed from Setup, Only ECC system memory allowed.

# Error message for memory decreased since last boot added.

# P01-0016

# Updated processor microcode for Intel Pentium ® Xeon ™ processors.

# Fix IRQ routing problem.

# B-0015

# Fix for IRQ9/AP CPU thrash

# Fix for PC97b WHQL v.7.6 in ACPI mode fails unreported I/O test failure.

# Fix for PC97b WHQL v.7.6  in ACPI mode fails on MS440GX  ECP printer port tests PC9x test failure

# Fix for PC97 ACPI test failure

# GX support for 2G added

# PnP OS setup question default to "NO"

# Removal of the user option to turn ACPI off within BIOS setup

# Added in Y2K

# Fix for ECC DMI event logging

# Fix for AC Power Loss

# Removed Option to boot in config mode

# B-0014

# Fix for APM hang at 400+ MHz

# B-0013

# Support for B0 Intel Pentium ® Xeon ™ Processors update

# B-0012

# Fix for MTRR programming above 512M

# Fix for PC97 compliance HCT test. Unreported Memory & IO test now pass.

# ACPI fan control now working and Soft SMI capability.

# Manufacturing Defaults for Resume on Ring changed.

# BIOS Spec Update rev 2.5 item E2 changed for 440GX chipset. (Performance increase)

# Resource file fix for CS4235 Audio chip

# Removed memory hole from setup

# Support for B0 Intel Pentium ® Xeon ™ Processors including strings.

# 440GX register programming incorporated for revision id checking and x11 column addressing.

# B-0011

# Readjusted fix for functional test issue with cache being disabled on first boot as stated below.

# Changed Mfg default for AC Loss to always Power on.

# B-0010

# Fixed Mfg Functional test issues with cache being disabled on first power up of board.

# Fixed Resume on ACLoss hang for “Stay Off” option.

# B-0009

# New Boot Block to support SPD added. (Fixes anomaly with Registered DIMM’s not working).  This Boot block also supports LS-120 drives with 3.5 inch legacy floppy media only.

# B-0008

# Changes for Fab B SMBUS addresses (DIMMs and Alertpack) and GPIO changes

# Note: Beta BIOS will not be supported on Fab A.

# A-0007

# Added support for Alert Pack

# Fix for Event Logging

# New Setup Organization

# Fix for Audio setup question not working. (Was always enabled)

# Fix for “On LAN”, “On PME”, and “On Modem Ring” setup questions functionality.

# Fix for “On AC Loss” setup question functionality.

# Fix for Flash always being write enabled.

# Fixed all DMI information and DMITEST passage.

# Fixed APMTEST hang problem.

# Fixed Invalid CPU speed settings in Configuration Mode.

# A-0006

# Boot block change only to allow for 440GX to work. (NOTE: Testing shows that only un-registered DIMMS seem to work with any Boot block released to this point. This includes all 440BX board builds as well.)

# A-0005

- New Features/Fixes

- Significant Phoenix Core changes incorporated. (VCM)

- Spanish and French Language Support

- Hard Disk Pre-delay

- Embedded PXE Support

- Legacy USB Support

- Extended Security Support

- 440BX Update S20, S28

- Wake on LAN

- ECC support (chipset only)

- Features not yet implemented

- Alert Pack

- GX Chipset

- ACPI

- Known Bugs

- DMI Event Logging does not function correctly

- Some DMI strings are not present

- BEL APM Test hangs the system

- Mixing DIMMS hangs the system at post code 28h

- Cache anomalies when put in configuration mode via jumper

- Resume on AC Loss - Stay Off test fails

- APM Front Panel Sleep Button

# A-0004

- Incorporated items in 440BX BIOS Spec. Update rev 2.3 (S3, S11, S17, S19, S27, S29, E2)

# A-0003

- Corrected GPO outputs for SIO 307 to TTL levels.

# A-0002

- Default L2ECC to enabled. Setup question removed

- Processor ucode id 19 added.

- SPD memory detection vs. Dynamic

- Fixed GPO for SDRAM EPROM write protect.

- Defaults for LAN, audio, and heceta changed to enabled.

- GPO’s for SIO 307 changed to TTL level outputs

# A-0001

- Using DYNAMIC memory detection to work due to problems with SPD which will eventually be put back into the bios.

- Changed the GPIO value for the SW_PCI_RESET signal to the Arbiter to a TTL compatible mode verse Open Drain